## Slide 1: Towards reducing total energy consumption while constraining core temperatures
Osman Sarood and Laxmikant Kale
Parallel Programming Lab (PPL)
University of Illinois Urbana Champaign

## Slide 2: Why Energy?
Data centers consume 2% of US Energy Budget in 2006
Costed $4.1 billion consumed 59 billion KWh
The 3-year cost of powering and cooling servers exceeds the cost of purchasing the server hardware
Notes: Data centers have been reported to have consumed energy equivalent to 2% of the total US energy budget in 2006
Their operation costed 4.1 billion and consumed a total of 59 billion
There have also been estimates to show that the cost of powering the server for only 3 years exceeds the cost of purchasing them
Now, although there has been a 2.5 times improvement in system level energy consumption, it is still far away from the 100 times improvement required for moving to exascale computing

## Slide 3: Cooling Energy
Cooling accounts for 40-50% of total cost
Most data centers face hot spots responsible for lower temperatures in machine rooms
Data center managers can save*:
  4% (7%) for every degree F (C)
  50% going from 68F(20C )to 80F(26.6C)
Earlier work:
  Reduce up to 63% in cooling energy with 11% penalty in execution time
  Constraining core temperatures below 44C
*according to Mark Monroe of Sun Microsystem
Notes: Cooling costs form a major part of the total energy budget for data centers. Infact they account for 50% of the total energy consumed
This high figure can also be attributed to hotspots which force data center operators to decrease the room temperature for the entire room
Studies show that for every 1C increase in room temperature, 7% of total cooling energy can be saved. In fact data centers can save half of the total cooling cost by raising the room temperature from 20C to 26.6C.
Data center operators can increase the room temperatures if they can be confident that there would be no hotspot formation and cpu cores wont reach very high temperatures.

## Slide 4: Machine Energy
Accounts for 50%-60% of total cost
Earlier work: limited machine energy savings
Is it possible to reduce execution time penalty and machine energy while constraining core temperatures?

## Slide 5: Core Temperatures
All results are on a quad core machine having Sandy Bridge Core i7-2600

## Slide 6: Frequency, Time and Power for NPB-FT
Reduce core power/temperature by reducing frequency with little impact on time

## Slide 7: Temperature Control - Naïve Scheme
Monitor temperature periodically
  Above threshold: decrease frequency
  Below threshold: increase frequency
Use DVFS to change processor voltage/frequency at runtime

## Slide 8: Naive Scheme – NPB-FT
Energy savings but timing penalty high!

## Slide 9
Can we do something to reduce the execution time penalty?

## Slide 10: Execution Blocks
Divide each iteration into Execution blocks (EBs)
  different sections based on sensitivity to frequency
  Manually done using HW performance counters
Profile each EB for different frequency levels
  Wall clock time (system clock)
  Core power consumption (fast on-chip MSRs)
EB 1
EB 2
EB 3
Iteration

## Slide 11: Execution Blocks (EBs) (NPB-IS)
EB1 much more sensitive to frequency with the same power as EB2
EB2 wastes a lot of energy while running at max frequency!

## Slide 12: EBTuner
Profile each EB for all frequency values
  Can be completed in milliseconds using energy MSRs of Sandy Bridge
Temperature > Threshold
  EB that results in minimum timing penalty
  Change its frequency down one notch
Temperature < Threshold
  EB that results in maximum time reduction
  Change its frequency up one notch

## Slide 13: Problem formulation
Minimize:
subject to:
Heuristic for best EB ( ):
Difference in power after reducing frequency
Difference in time after reducing frequency
Maximize ratio for temperature > T_max

## Slide 14: EBTuner: Framework
EB 1
EB 2
Iteration
Profiler
Frequency Control
Frequency Control
EBTuner
Very fast using MSR energy counters
Runs each EB at the specified frequency
Determines if the temperature crosses threshold
Specifies new frequency for each EB
Temp Check

## Slide 15: Evaluation
On a single quad core machine
Metrics
  Ability to constrain core temperature
  Timing penalty
  Reduction in energy consumption

## Slide 16: Temperature Control
Using EBTuner - Temperature Threshold 54C

## Slide 17: Timing penalty
Increase in execution time compared to runs with no temperature control and all cores working at maximum possible frequency

## Slide 18: Steady State Frequencies
Counter | NPB-LU | NPB-FT
MFLOPS | 1032 | 640
L1-L2 (MB/sec) | 2114 | 2416
L2-L3 (MB/sec) | 3365 | 6806
Penalty (%) | 6 | 6
~ 400MHz
Using EBTuner - Temperature Threshold 54C

## Slide 19: Variance in sensitivity to frequency for different parts of an application
Correlation

## Slide 20: EB Tuner Vs. Naïve (NPB-IS)
EBTuner increases CPU utilization

## Slide 21: Reduction in machine energy

## Slide 22: Energy Time tradeoff
: 0.19
: 0.55
: 0.53

## Slide 23: Summary and Future Work
Our scheme consistently better than Naïve version in terms of reducing timing penalty and machine energy consumption
EBTuner was able to reduce machine energy by 17% with <1% timing penalty while constraining core temperature below 60C
Combine this work with earlier work that saves cooling energy consumption

## Slide 24: Thank You
Questions?