## Slide 1: Toward Runtime Power Management of Exascale Networks by On/Off Control of Links
Ehsan Totoni
University of Illinois-Urbana Champaign, PPL
Charm++ Workshop, April 16 2013

## Slide 2: Power challenge
Power is a major challenge
Blue Waters consuming up to 13 MW
  Enough to electrify a small town
  Power and cooling infrastructure
Up to 30% of power in network
  Projected for future by Peter Kogge
  Saving 25% power in current Cray XT system by turning down network
    Work from Sandia

## Slide 3: Network link power
Network is not “energy proportional”
  Consumption is not related to utilization
  Near peak most of the time
  Unlike processor
Recent study:
  Work from Google in ISCA’10
  50% of power in network of non-HPC data center
  When CPU’s underutilized
Up to 65% of network’s power is in links

## Slide 4: Exascale networks
Dragonfly
  IBM PERCS in Power 775 machines
  Cray Aries network in XC30 “Cascade”
  DOE Exascale Report
High dimensional Tori
  5D Torus in IBM Blue Gen/Q
  6D Torus in K Computer
Higher radix -> a lot of links!

## Slide 5: Communication patterns
Applications’ communication patterns are different
Network topology designed for a wide range of applications
MILC
NPB CG

## Slide 6: Fraction of links ever used

## Slide 7: Nearest neighbor usage

## Slide 8: More expensive links

## Slide 9: Nearest neighbor

## Slide 10: Solution to power waste
Many of the links are never used
  For common applications
Are networks over-built? Maybe
  FFTs are crucial
  But processors are also overbuilt
Let’s make them “energy proportional”
  Consume according to workload
  Just like processors
Turn off unused links
  Commercial network exists (Motorola)

## Slide 11: Runtime system solution
Hardware can cause delays
  According to related work
  Not enough application knowledge
    Small window size
Compiler does not have enough info
  Input dependent program flow
Application does not know hardware
  Significant programming burden to expose
Runtime system is the best
  mediates all communication
    knows the application
    knows the hardware

## Slide 12: Feasibility
Not probably available for your cluster downstairs
  Need to convince hardware vendors
  Runtime hints to hardware, small delay penalty if wrong
Multiple jobs: interference
  Isolated allocations are becoming common
    Blue Genes allocate cubes already
  Capability machines are for big jobs

## Slide 13: Software design choices
Random mapping and indirect routing have similar performance but different link usages

## Slide 14: Power model
We saw many links that are never used
Used links are not used all the time
  For only a fraction of iteration time
  Compute-communicate paradigm
A power model for “network capacity utilization”
  “Average” utilization of all the links
  Assume that links are turned magically on and off
    At the exact right time
  No switching overhead
  Example: network used one tenth of iteration time

## Slide 15: Model results

## Slide 16: Scheduling on/offs
Runtime roughly knows when a message will arrive
  For common iterative HPC applications
  Low noise systems (e.g. IBM Blue Genes)
There is a delay for switching the link
  10μs for current implementation
  Much smaller than iteration time
  Runtime can be conservative
    Schedule “on”s earlier
    Similar to having more switching delay

## Slide 17: Delay overhead

## Slide 18: Results summary

## Slide 19: Questions?
Are you convinced?