## Slide 1: Cache Hierarchy Reconfiguration in Adaptive HPC Runtime Systems
Ehsan Totoni
Josep Torrellas
Laxmikant V. Kale
Charm Workshop
April 29th, 2014

## Slide 2: Exascale Power Challenge
Tianhe-2
~34 PFlop/s Linpack
~18 MW power
Goal: ExaFlop/s at 20MW
~26 times more energy efficiency needed
Top500.org November 2013

## Slide 3: Caches
Caches consume a large fraction of processor’s power
  40% in POWER7, after many techniques
Getting larger every day
  Intel Xeon E7-88702: 30MB of SRAM L3
  IBM POWER8: 96MB of eDRAM L3
Fixed design, but applications are different
  E.g. potentially no locality in pointer chasing “Big Data”

## Slide 4: Cache Energy Waste
Scenario: NAMD on Blue Waters
  HIV simulations, only 64 million atoms
    48 bytes atom state (position & velocity)
    Some transient data (multicasts)
    Assuming 400 bytes/atom, 25.6 GB
  4000 Cray-XE nodes
    32 MB of L2 and 32 MB L3 each -> 256 GB of cache!
    90% of capacity not unused
    (there is nothing wrong with NAMD!)
  16 days wall clock time, not best use of caches.. Huge waste!

## Slide 5: Cache Reconfiguration
Turning off cache ways to save energy proposed
Two main issues:
  Predicting the applications future
  Finding the best cache hierarchy configuration
We solve both on HPC systems

## Slide 6: HPC Systems
Many processors are commodity
  Not necessarily designed for HPC
Provisioning different than non-HPC
  No multi-programming, time-sharing, co-location
  Large, long jobs
  High Predictability

## Slide 7: HPC Applications
Properties of algorithms in common HPC apps:
  Particle interactions (MiniMD and CoMD)
    Force computation of entities
    Small domain, high temporal locality
  Stencil computations (CloverLeaf and MiniGhost)
    Update of grid points with stencils
    Large domain, low temporal locality
  Sparse Linear Algebra (HPCCG, MiniFE, and MiniXyce)
    Update of grid points with SpMV
    Often large domain, low temporal locality

## Slide 8: Stencil Access Pattern

## Slide 9: Adaptive RTS Approach
HPC applications are iterative
  Persistence: Same pattern repeats
  RTS can monitor application, predict future
Single Program Multiple Data (SPMD)
  Different processors doing the same thing
  RTS can try cache configurations exhaustively
RTS can apply best cache configuration
  Monitor, re-evaluate regularly

## Slide 10: Reconfiguration Units
RTS tracks Sequential Execution Blocks (SEBs)
  Computations between communication calls
Identified by characteristic information
  Communication calls and their arguments
  Duration
  Key performance counters
Usually repeated in every iteration

## Slide 11: MILC’s Pattern
Hierarchical iteration structure
PE 0
PE 3
PE 1
PE 2
Overall iteration
subiter

## Slide 12: Identifying Iteration Structure
RTS needs to identify iterative structure
  Difficult in most general sense
Using Formal Language Theory
  Define each SEB as a symbol of an alphabet Σ
  An iterative structure is a regular language
    Easy to prove by construction
  Each execution is a word

## Slide 13: Pattern Recognition
In profiling, RTS sees a stream of SEBs (symbols)
  Needs to recognize the pattern
  Learning a regular language from text
  Build a Deterministic Finite Automaton (DFA)
Prefix Tree Acceptor (PTA)
  A state for each prefix
  Not too large in our application

## Slide 14: Evaluation Methodology
Mantevo mini-app suite
  Representative inputs
  Assume MPI+OpenMP
  Identify unique SEBs
SESC cycle-accurate simulator
  Simulate different configurations for each SEB
Model cache power/energy using CACTI

## Slide 15: Evaluation Results
Format: <ways turned on>/<total number of ways>
Best configuration depends on:
Application type
Input size

## Slide 16: Evaluation Results
5% Performance Penalty Threshold
67% cache energy saving (28% in processor) on average

## Slide 17: Adapt to Problem Size
Adapting to problem size is crucial.

## Slide 18: Reconfigurable Streaming
Streaming: predict data and prefetch for simple memory access patterns
  Two important parameters:
  Cache size to use
  Prefetch depth
Can waste energy and memory bandwidth
  Too deep/small cache evicts useful data
  Prefetch enough data to hide memory latency

## Slide 19: Reconfigurable Streaming
RTS can tune cache size and depth
  Similar to previous discussion
Hardware implementation:
  Prefetcher has an adder to generate next address
  One input can be controlled by RTS as a system register
  Does not have overheads of repetitive prefetch instructions

## Slide 20: Performance/Energy Tradeoff
Small gains in performance might have high energy cost

## Slide 21: Hardware Complexities
Wrong speculative path is accelerated with deeper prefetch
Intervenes with useful computation

## Slide 22: Related Work
Automatic cache hierarchy reconfiguration in hardware had been explored extensively
  Survey by Zang and Gordon-Ross
  Hardware complexity -> energy overhead
  Hard to predict application behavior in hardware
    Small “window”
    Choosing best configuration
Compiler directed cache reconfiguration (Hu et al.)
  Compiler’s analysis is usually limited
    Many assumptions for footprint analysis
      Simple affine nested loops
      Simple array indices (affine functions of constants and index variables)
    Not feasible for real applications

## Slide 23: Conclusion
Caches consume a lot of energy (40%>)
Adaptive RTS can predict application’s future
  Using Formal Language Theory
Best cache configuration can be found in parallel (SPMD model)
  67% of cache energy is saved on average
Reconfigurable streaming
  Improves performance and saves energy
  30% performance and 75% energy in some cases

## Slide 24: Future Work
Prototype machine (MIT Angstrom?) and runtime (Charm++ PICS)
Find best configuration in small scale
  When exhaustive search is not possible
  Using common application patterns
Extend to mobile applications
  Many modern mobile apps have patterns similar to HPC!

## Slide 25: Cache Hierarchy Reconfiguration in Adaptive HPC Runtime Systems
Ehsan Totoni
Josep Torrellas
Laxmikant V. Kale
Charm Workshop
April 29th, 2014