## Slide 1: OpenAtom: On the fly ab initio molecular dynamics on the ground state surface with instantaneous GW-BSE level spectra
PIs: G.J. Martyna, IBM; S. Ismail-Beigi, Yale; L. Kale, UIUC;
Team: Q. Li, IBM, M. Kim, Yale; S. Mandal, Yale;
E. Bohm, UIUC; N. Jain, UIUC; M. Robson, UIUC; E. Mikida, UIUC; P. Jindal, UIUC; T. Wicky, UIUC.
1
Light in

## Slide 2
Outline:
Introduction to the OpenAtom project
Statistical sampling of complex systems on the ground state surface
Optimization under charm++
GW-BSE – a new charm++ application.
Light in
2

## Slide 3: IBM : A History of Multidisciplinary Research
2012 Excimer Laser Surgey (Nation Medal of Technology)
2009 Nano MRI
World’s First Petaflop Supercomputer
Francis Allen: 1st Female Turing Award winner & 1st Female IBM Fellow
Cell Architecture
2004 Blue Gene (National Medal of Technology)
2003 Carbon Nanotube Transistors
1997 Copper Interconnect Wiring
1994 Silicon Germanium (SiGe)
1987 High-Temperature Superconductivity (Nobel Prize)
1986 Scanning Tunneling Microscope (Nobel Prize)
1980 RISC
1971 Speech Recognition
1970 Relational Database
1967 Fractals
One-Device Memory Cell
1965 FFT (Cooley and Tukey).
1957 FORTRAN (Program lang)
RAMAC (comput. w. mag. disk)
IBM’s Watson Cognitive Computer
D. Ferrucci Wild Duck
“Treasure wild ducks”
James Watson, Jr.
(from Kierkegaard)
www-03.ibm.com/ibm/history/ibm100/us/en
Exploratory work: Yorktown, Almaden & Zurich
Science & Solutions
3

## Slide 4
Power is limiting progress in the IT world – CMOS has reached fundamental limits.
Data-centric: communication is expensive.
Dark silicon/on-chip power savings will not deliver enough savings - Microsoft Project Natick – underwater data centers!!!!!! (projectnatick.com)
Sensor revolution requires on-board low-power computing to preprocess
data avoiding power cost of wireless communication.
The spectrum is congested and/or contested.
Higher performance electronics for agile radars and communications are needed to move forward - RF FPGA’s
Power: A Cause for Concern
Where is IT today and where is it going?
IT industry has driven giant productivity gains in the last 40 years – are we done?
Wireless Communication and Radar: New demands for high performance
IT continues like
Electrification??
New efficient methodology and implementations required for progress!
It’d better!!
4

## Slide 5
Philosophy: Statistical Sampling of Complex
Environments is Key to Understanding many Physical Systems across Science and Solutions
Biological function is enabled by fluctuations in both the environment and the biomolecules.
Pollutant detection requires sampling complex aqueous systems and then exporting the results to a GW/GW-BSE app for computation of spectra.
Understanding chemical reactions in dense arrays
requires non-trivial sampling of the full system due to complex many-body reaction paths.
Light in
5

## Slide 6: Simulating materials with atomic detail on the Ground State Born-Oppenheimer Surface: Reaching Long Time Scales via Parallel Software and Novel Physics Based Methodology
PI: Glenn Martyna, IBM TJ Watson Research Center,
Honorary Professor of Physics, University of Edinburgh,
2016 IPAM Senior Fellow
Postdoc: Qi Li, IBM TJ Watson Research Center
6
Light in

## Slide 7
Goal : The accurate treatment of complex heterogeneous
systems to gain physical insight.
Light in
7

## Slide 8
Where we were at the start of the project from previous collaboration with Kale group:
OpenAtom
Charm++ implementation of the Car Parinello Ab initio Molecular
Dynamics based on KS-DFT within Generalized Gradient Approx.
Features include:
  Order N2 log(N) Euler Exponential Spline (EES) method for norm conserving non-local pseudopotentials.
  Order N log(N) EES method for local pseudopotential and Ewald interactions.
  High parallel scaling on BlueGene/L and BlueGene/P (10k procs).
  Roughed in path Integrals, k-point sampling, LSDA and parallel tempering sampling.
  Parallel 3D-FFTs handwritten by scientists.
Great for main group systems, achieve nanosecond time scales- a breakthrough in its day (just a few years ago)!
IBM Journal of Research and Development 52 (1.2), 159-175 (2008).
8

## Slide 9
Transparent Conducting Electrodes (TCEs)
for thin film amorphous silicon solar cells
Conventional TCEs:
Indium Tin Oxide (ITO)
Zinc Oxide (ZnO)
Graphene TCEs:
1 – 8 atomic layers
Performance:
Transparency 95%
Sheet resistance 10W
Manufacturing:
Performance:
Transparency 85%
Sheet resistance 100W
Manufacturing:
cm X cm size sheets
Science, 324, p. 1312 (2009).
Light in
9

## Slide 10
Goal
Engineering goal
Experimental data: G. Tulevski (IBM), A. Kasry (EGNC), A. Boll (IBM)
ACS nano 4 (7), 3839-3844 (2010)
# layers
Doping mechanism?
How to meet goal?
10

## Slide 11: 6SbCl5 +C84  C842+(2SbCl6-) + SbCl3 + 3SbCl5
11
ACS nano 5 (4), 3096-3103 (2011)

## Slide 12
Project Goals: Improve sampling, accuracy, applicability and parallel performance of OpenAtom to achieve breakthrough performance
Transition Metals: Plane Augmented Wave method, LSDA, k-point sampling.
Reactive Chem: Hybrid functionals (beyond GGA) – Exact exchange (HF).
Nuclear Quantum Effects: Path Integral Molecular Dynamics.
Sampling Rough Energy Landscapes: Parallel tempering (PT).
Metric Factors : Improve baseline CPAIMD with phase space metrics (PSM).
Extension to Analytics: Use power of OpenAtom in Discovery Projects.
Addressing complex systems and sampling problems requires
significant collaborative development!!!!
OPENATOM
12

## Slide 13
UIUC tasks:
3D-FFT library – beyond GJM.
Flow of control refactor.
Bringing Tempering, Path integrals, k-points, LSDA to life – “Übers”.
Parallelization of “Übers”.
GPGPUs for orthogonality.
Parallelization of “Advanced methods” (PAW, HF, PSM, …).
IBM tasks:
Derive order N2 log(N) PAW.
Implement Grimme van der Waals.
Derive reduced order HF exch.
Derive selection rule for parallel tempering on sampled potential surfaces – penalty method.
Derive improved CPAIMD via PSM.
Write toy codes and scientific papers.
Joint work:
Framework new methods.
Implement new methods.
Develop test suite for new methods – implement in OpenAtom’s Jenkins app.
Apply OpenAtom to important systems across S&T .e.g.
Metal Organic Framework with Yale & UIUC.
Project Goals: Improve sampling, accuracy, applicability and parallel performance of OpenAtom
Hero System
13

## Slide 14
Reduced order Hartree-Fock Exchange for Extended States – in 3 minutes or less
Challenge: Reduced order methods for HF exchange are all formulated
for localized states. Metal-insulator transitions,
Metal-Semiconductor-Metal junctions → “no-go”.
Solution: A collaboratively developed r-space outer product formulation
motivates a new r-space/g-space decomposition to
reduce HF exch. computational complexity by N2/3, N3 → N7/3 for the plane-wave (pw) basis.
14

## Slide 15
The proof – in a nutshell (2 slides)
HF exch. under PBC:
sum over periodic
images, m.
Outer product of orbitals on
the discrete pw mesh ~ N3.
Following Ewald - insert long/short-range decomp. of Coulomb interaction.
1st image
sufficient
15

## Slide 16
The proof – in a nutshell (2 slides)
Simplify* and introduce matrices on coarse, , and fine , meshes:
Create sparse-matrix on fine mesh: N2 ~ N2
Create dense-matrix on coarse mesh: N3 ~ N3
Choose α to equalize scaling: N7/3 (add log N for FFT’s)
FFT’s
16
*

## Slide 17
Complexity of short-range part governed by cutoff radius in u-space
through erfc(), <~
Complexity of long-range part governed by cutoff radius in g-space through exp(~ [1]
Equating gives
which in turn yields the desired scaling of the short/long-range parts
~ =
Reduced order Hartree-Fock Exchange: Scaling
[1] A plane wave basis with cutoff contains basis functions where V~N.
17

## Slide 18
  Short-range HF exchange requires treating an integrable singularity (Coulomb)
  The plane wave mesh is equally spaced in Cartesian coordinates.
  Develop a method to treat integrable singularities on simple meshes.
Reduced order Hartree-Fock Exchange: Accuracy
18
Consider integration in 1 spatial dimension for simplicity:
Introduce a 1st order interpolation of f(x) in each cell
where and = (). This can be input into and the integral over x performed analytically. Combing terms, the 1st order approximation to I, is
where for k(x)=1 the result is trapezoidal rule integration and K(i) is the “grid” function of k(x). This is employed only in cells where k(x) is rapidly varying – otherwise trap. rule integration of product function, f(x)k(x), is used,
)
Integration pts on edge
Short-range
Coulomb over
a Gaussian density
Model for 32 waters (ambient conditions)
at 70 Ry pw cutoff
3D Generalization
of equally spaced
3D-Cartesian grid

## Slide 19
Reduced order Hartree-Fock Exchange: Sizing
System of interest : 32 water molecules under ambient conditions in a L=9.86 on edge cell with a 70 Ry pw cutoff sets the fine pw grid to be ≈100 points on edge.
Take: (1) the fine grid u-space cutoff: = 3.5/
(2) the sparse grid g-space cutoff: = 7
Choose: =21.5/L
Estimate: New method saves ≈70x compared a N3 computation
(.i.e. g-space treatment on the fine pw grid, lim ).
Validate: Cutoff choices and timing estimates need testing in the “real world” where overhead, truncation error etc. matter.
19
9.86

## Slide 20
UIUC tasks:
3D-FFT library – beyond GJM.
Flow of control refactor.
Bring Tempering, Path integrals, k-points, LSDA to life – “Übers”.
Parallelization of “Übers”.
GPGPUs for orthogonality.
Parallelization of “Advanced methods”
(PAW, HF, PSM, …).
IBM tasks:
Derive N2 log(N) scaling PAW.
Implement Grimme van der Waals.
Derive reduced order HF exch.
Derive selection rule for parallel tempering with sampled. potential surfaces – penalty method.
Derive improved CPAIMD via PSM.
Write toy codes and scientific papers.
Joint work:
Framework new methods.
Implement new methods.
Develop test suite for new methods – implement in OpenAtom’s Jenkins app.
Apply OpenAtom to important systems across S&T,
e.g. Metal Organic Framework with Yale & UIUC.
Develop analytics application for discovery.
Progress towards project goals
Hero System
accomplished
ongoing
TBD
20

## Slide 21: OpenAtom Ground State Software Overview
PPL Contributors: Eric Bohm, Nikhil Jain, Prateek Jindal, Eric Mikida, Michael Robson

## Slide 22
Software Infrastructure
GIT (Gerrit) based repository:
  http://charm.cs.illinois.edu/gerrit/openatom
  Or https://github.com/ericbohm/OpenAtom/
Test system datasets available in git
  Make test - Basic feature verification
  Make full_test - Extensive use case verification
Jenkins testing
  Release branch in nightly Charm++ testing
  Release branch in Charm++ continuous integration testing

## Slide 23
Ground State Feature Status
Feature | Minimization Status | Dynamics Status | Test Integration
CPAIMD Dynamics | NA | Production | Automated
Path Integrals | Production | Production | Automated
K-Points | Production | Needs Verification | Manual
Spin Orbitals | Production | Production | Manual
Tempering | NA | Production | Manual
Born Oppenheimer Dynamics | NA | Production | Automated
Band Generation | Needs Verification | Needs Verification | Manual

## Slide 24
Data Structures and control flow in OpenAtom

## Slide 25: Object Decomposition
Showing a subset of object collections

## Slide 26: Object Placement
Nikhil Jain

## Slide 27: Topology aware mapping

## Slide 28: Adapting to different systems
Separate the logical operations and machine-specific operations. Example:
  Logical operation: get an ordered list of nodes
  Machine specific: Hilbert curve traversal, blocked traversal, plane-traversal
Density FFTs: require use of full bisection bandwidth – spread throughout the allocation.
Matrix-matrix multiplies (pair calculators): place near the GSpace planes, but load balance is important.

## Slide 29: System utilization without mapping (barriers introduced for clarity)
States: Many
G -> R FFTs
Density: G -> R -> G
Non-local G-> R -> G
Density to States
States R-> G
Force correction
Ortho-normalizaton

## Slide 30: System utilization with mapping

## Slide 31: Impact of mapping on Blue Gene/Q: up to 30% improvement

## Slide 32: Impact of mapping on Blue Waters: up to 32% improvement

## Slide 33: Charm FFT
Nikhil Jain

## Slide 34: Optimizing FFTs in the density
Charm-FFT implemented to help improve the performance of the density phase.
Features:
  Concurrent FFTs
  2D decomposition
  Overlaps with other work
  Cutoff aware
  Mapped by the application

## Slide 35: Simulating 32 molecules of Water on Blue Waters

## Slide 36: Multi-Instance Methods
Eric Bohm

## Slide 37
Multi Instance Methods
Retain all existing code with minimal changes
Any feature available for CP minimization or dynamics automatically available for multi-instance use
Add Master Index of objects
  Uber[temper][bead][k-point][spin]
  Objects in any instance can be referenced by any object
  Support simulations with many kinds of multi instance physics
  Instance Controller
  Temper Controller
    Sum energies across Tempers and Beads
    Switch Energies and Temperatures
  Bead Controller
    Intrapolymer force evaluation and integration

## Slide 38: Spin Orbitals (LSDA)
Each Spin shares : atom and energy chares
Electron density from down passed to up
  VKS computed for each spin
  Returns to standard flow of control
Independent I/O for state data
Independent placement for instance chares

## Slide 39: K-Points
Each k-point shares:
  electron density, atoms, energy chares
Electron density = sum over KP electron states
Wave functions outside the first Brillouin zone forces use of complex (e.g., ZGEMM)
  Instead of the “doublepack” optimization used at the Γ point
Independent I/O for state data
Independent placement for electron state instance chares
ρ

## Slide 40: Path Integral Beads
Path Integral Bead replica contains independent instances of all phases of CPAIMD
  May contain k-point and spin ensembles
Intrapolymer force evaluation in PIBeadAtoms
  Interacts with each Bead instance's AtomsCompute
  Supplements CPAIMD nucleic force integration phase
  Computation Parallelized across NumAtoms and NumBeads
Independent I/O for state and coordinate data
Independent placement for instance chares
Bead1
Bead2
Bead4
Bead3
Bead5
Bead6
Bead
Ctrl

## Slide 41: Path Integral Performance

## Slide 42: Multi Instance Challenge: cross bead interference

## Slide 43: Cross FFT Interference

## Slide 44: After Scheduling Improvements

## Slide 45: Tempers
Contains independent instances of all phases of CPAIMD
Each temper may contain Beads, K-points, and Spin instances
Temper controller manages random neighbor shuffle to exchange temperatures across temper replicas
Independent I/O for state and coordinate data
Independent placement for instance chares
280⁰
290⁰
300⁰
310⁰

## Slide 46: Temper Performance

## Slide 47: Combined Performance

## Slide 48: GPGPU
Michael Robson

## Slide 49: Opportunities for GPUs
PC
PC
PC
PC
ORTHO

## Slide 50: Ortho Integration
T = S-½
Kernel developed by summer intern
Changes from distributed to centralized
Gather pieces of S from PCs
S -> T

## Slide 51: Opportunities for GPUs
Orthonormalization (Ortho)
  Inverse Square Root of Matrix
Pair Calculator (PC)
  Matrix Matrix Multiplication
Both make good GPU targets

## Slide 52: Results for MOF System
1 iteration, 1PE, 64 XK Nodes of Blue Waters
Centralized Ortho, No CUDA
Centralized Ortho, CUDA
Distributed Ortho, No CUDA
148 ms
210 ms
174 ms
153 + 1684 ms
198 + 69 ms
75 + 88 ms
Notes: Late Breaking Results: Competitive!

## Slide 53: Results for 256 Water Molecules
1 iteration, 1 PE, 64 XK Nodes of Blue Waters
Centralized Ortho, No CUDA
Centralized Ortho, CUDA
Distributed Ortho, No CUDA
296 ms
312 ms
78 ms
297 + 2781 ms
297 + 105ms
72 + 172 ms
Notes: 2 Logical Node Example

## Slide 54: Pair Calculator Results
Baseline CUBLAS implementation
  Offload forward and backward multiply
  CUDA Streams
  Directly allocate memory
  Synchronize on data move
  Fine because we don’t have other work

## Slide 55: Results for 256 Water Molecules
1 iterations, 1 PE, 64 XK Nodes of Blue Waters
Baseline
CUBLAS
164 ms
47 ms
205 ms
113 ms
90 ms
142 ms
163 ms
216 ms
 | Forward | Speedup
Baseline | 327 ms | 
CUBLAS | 137 ms | 2.39x
Backward | Speedup
421 ms | 
255 ms | 1.65x
Per Iter | Speedup
2.582796 s | 
2.346571 s | 1.10x
Notes: 2 Logical Node Example

## Slide 56: Ground State Future Work
Test automation and feature verification
Multi-Instance Performance Tuning
CharmFFT integration for State and Non-local
Fast Hartree Fock
PAW
GPU
  GPU Manager integration
  Backward path PC
  CharmFFT
  Communication optimization (NVLink, etc)
Auto-tuning controls in PICS

## Slide 57
Subhasish Mandal1, Minjung Kim1, Eric Mikida2, Eric Bohm2, Prateek Jindal2, Nikhil Jain2, Laxmikant V. Kale2, Glenn Martyna3,
& Sohrab Ismail-Beigi1
1Dept. Of Applied Physics, Yale University
2Department of Computer Science, University of Illinois at Urbana–Champaign
3IBM T. J. Watson research Center
Towards high scalable GW calculations

## Slide 58
Towards high scalable GW calculations
OpenAtom + GW
git clone http://charm.cs.illinois.edu/gerrit/openatom.git
University of Illinois
IBM Watson Research
Yale University

## Slide 59: Outline
Introduction & Motivation of GW
Stages of GW calculation
Static Polarizibility : Methods & Scaling
Computing self-energy S(w)
Summary

## Slide 60: GW-BSE: what is it about?
DFT is a ground-state theory for electrons
But many processes involve exciting electrons:
Transport of electrons in a material or across an interface: dynamically adding an electron
 The other electrons respond to this and modify energy of added electron
e-
“GW” method solves this problem

## Slide 61: Successes of GW
Energy gaps (eV)
* Hybertsen & Louie, Phys. Rev. B (1986)
Material | DFT-LDA | GW* | Expt.
Diamond | 3.9 | 5.6 | 5.48
Si | 0.5 | 1.3 | 1.17
LiCl | 6.0 | 9.1 | 9.4

## Slide 62
GW-BSE is computationally challenging:
Huge number of FFTs
Huge memory footprints
Large and dense matrix multiplications
Theoretical scaling | 
DFT: | N3
GW: | N4
BSE: | N6
Ex. 50-75 atoms (GaN) | 
DFT: | 1 cpu x hours
GW: | 91 cpu x hours
BSE: | 2 cpu x hours
Goal:
Developing highly scalable GW-BSE software
to tackle these challenges
Motivation (Cont. )

## Slide 63
Zinc oxide nanowire
P3HT polymer
But with available GW-BSE methods
it would take “forever”
i.e. use up all my supercomputer allocation time
Motivation (Cont. )
Would love to do GW-BSE on this photovoltaic system…

## Slide 64
GW
Dyson equation for many-body problem:
self-energy
GW Equation:
Hedin, Phy Rev, 139, 1965; Hybertsen, Louie, PRB, 34,1986
=E
=E
Physicist’s favorite :

## Slide 65: Stages of GW calculation
Stage 1 : Run DFT calc. on structure  output : Ei and 𝜓i(r)
Stage 2.1 : compute Polarizability matrix
Stage 2.2 : double FFT rows and columns  P(G,G’)
Stage 3 : compute and invert dielectric screening function
Stage 4 : “plasmon-pole” method  dynamic screening
Stage 5 : put together Ei , 𝜓i(r) and  self-energy S(w)

## Slide 66: Hardest parts
Stage 1 : Run DFT calc. on structure  output : Ei and 𝜓i(r)
Stage 2.1 : compute Polarizability matrix
Stage 2.2 : double FFT rows and columns  P(G,G’)
Stage 3 : compute and invert dielectric screening function
Stage 4 : “plasmon-pole” method  dynamic screening
Stage 5 : put together Ei , 𝜓i(r) and  self-energy S(w)
Most expensive

## Slide 67
Standard G-space approach:
Directly compute P in G space
A huge number of FFTs (NvNc)
Nv : # occupied states
Nc : # unoccupied states
R-space approach: Much fewer number of FFTs
Static Polarizability

## Slide 68
New R-space approach:
# FFTs: Nr
1) Calculate static polarizability in real space
2) FFTs for columns
3) FFTs for rows
# FFTs: Nr
Nr: # R grid
Nr ≈ 4Nc
 | G-space approach | R-space approach
#FFT | NvNc | 8Nc
Nv=500 Nc=1,500 | 750,000 | 12,000
Nv : # occupied states
Nc : # unoccupied states
Static Polarizability

## Slide 69
Si crystal
Dense FFT grid: 24×24×24
P and ε-1 converge at: 12×12×12
What R grid should we use?:
Chart: Size of FFT grid (N×N×N)
| 8.0 | 10.0 | 12.0 | 14.0 | 16.0
 | -0.010125 | -0.023178 | -0.029505 | -0.029505 | -0.029505
N
reduced to 1/8 !!
3D FFT box
Static Polarizability
Notes: Add another materials

## Slide 70: Test system
Si bulk
Total number of atom : 54
108 occupied states
892 unoccupied states
3 k-points
289,008 total f vectors
Each state and f vector ~0.5 MB
Scaling of Polarizibility

## Slide 71: Performance
SMP: shared memory programming: takes advantage of node level parallelism
Calculation | Time (seconds) | 
 | SMP, BLAS3 (2D decomposition) | No SMP, BLAS 2 (1D decomposition)
Compute f vectors for a single unocc state | 0.005 | 0.08
Total for 2,676 sets of f vectors | 14.17 | 378.04
Total wall time | 105.79 | 416.22
Overhead (comm, synchronization) | 90.50 | 38.18
* Results on 1024 nodes of Vesta, 32 threads per node
Eric M, UIUC

## Slide 72
Performance
Total Wall Time (Seconds)
Number of Nodes
32 Threads per node on Vesta
Computing P-matrix

## Slide 73
Stage 5 : Put together Ei , 𝜓i(r) and  self-energy S(w)
GW-Self-Energy (S)

## Slide 74
GW-Static Self-Energy (COHSEX)
Static self-energy approximation: a useful simplification
W(r,r’,E)  W(r,r’,E=0)=W(r,r’)
=

## Slide 75
GW-Static Self-Energy (COHSEX)
Static self-energy approximation: a useful simplification
W(r,r’,E)  W(r,r’,E=0)=W(r,r’)
Band Gaps (eV) |  |  |  |  | 
System | Experiment | DFT-LDA | COHSEX | Corrected COHSEX* | GW(full)
Diamond | 5.48 | 4.20 | 6.99 | 5.93 | 5.70
Si | 1.17 | 0.49 | 1.70 | 1.18 | 1.29
*Kang & Hybertsen, Phy Rev B, 82, 2010

## Slide 76
GW-Bare Exchange
Coulomb
Strategy 1:
(Motivated from P(G,G’) )
Coded and tested
v
‘
Double FFT
Strategy 2:
Coded and tested
Single FFT

## Slide 77
GW In-house code
Real time required on Si calculation:
135.369 sec
Real time required on Si calculation:
2.783 ssec
FFT of vector
FFT of rank 2 matrix
Strategy 2 wins
GW-Bare Exchange
Strategy 1:
Strategy 2:
Screened Exchange: followed with Strategy 2
Coulomb-Hole: followed with Strategy 2

## Slide 78: Summary
Acknowledgement
New R-space approach of Polarizibility
Polarizibility is parallelized with Charm++ & take the advantage of SMP
We have investigated various ways to calculate static self-energy.
Strategy 1 is effective for P(G,G’) But for COHSEX Strategy 2 wins
NCSA & ALCF@Argonne National Laboratory.
QUESTION ?

## Slide 79
Static polarizability calculations
Standard G-space approach:
Directly compute P in G space
A huge number of FFTs (NvNc)
Nv : # occupied states
Nc : # unoccupied states
The most time consuming part
R-space approach: Much fewer number of FFTs

## Slide 80
GW-Static Self-Energy (COHSEX)
Static self-energy approximation: a useful simplification
W(r,r’,E)  W(r,r’,E=0)=W(r,r’)
=

## Slide 81
GW-Bare Exchange
Coulomb
Strategy 1: Motivated from P(G,G’)
Sum over l & compute:
Strategy 1:
Coded and tested
v
‘
Double FFT

## Slide 82
GW-Bare Exchange
Strategy 2:
Compute fr (vector) and do FFT:
Multiply: vg fg fg’ and take sum over g
Strategy 2:
Coded and tested
v

## Slide 83: Density Functional Theory
For the ground-state of an interacting electron system we solve a Schrodinger-like equation for electrons
Hohenberg & Kohn, Phys. Rev. (1964); Kohn and Sham, Phys. Rev. (1965).
Approximations needed for Vxc(r) : LDA, GGA, etc.
Tempting: use these electron energies ϵj
to describe processes where
electrons change energy
(absorb light, current flow, etc.)

## Slide 84: Step 2 – FFT P to G-Space
FFT each row of P locally:
Transpose P
FFT each row locally again
Transpose P again:
Total time: 13.93s
Performance
* Results on 1024 nodes of Vesta, 32 threads per node

## Slide 85
GW In-house code
Real time required on Si calculation:
135.369 sec
Real time required on Si calculation:
2.783 ssec
FFT of vector
FFT of rank 2 matrix
Strategy 2 wins
GW-Bare Exchange
Strategy 1:
Strategy 2:
Summary:
Screened Exchange:
=
Coulomb-Hole:

## Slide 86
GW-Static Self-Energy (COHSEX)
Static self-energy approximation: a useful simplification
W(r,r’,E)  W(r,r’,E=0)=W(r,r’)
Band Gaps (eV) |  |  |  |  | 
System | Experiment | DFT-LDA | COHSEX | Corrected COHSEX* | GW(full)
Diamond | 5.48 | 4.20 | 6.99 | 5.93 | 5.70
Si | 1.17 | 0.49 | 1.70 | 1.18 | 1.29
*Kang & Hybertsen, Phy Rev B, 82, 2010
=

## Slide 87: Scaling of Polarizibility
Stage 2.1 : compute Polarizability matrix
Stage 2.2 : double FFT rows and columns  P(G,G’)
Most expensive

## Slide 88
GW-Bare Exchange
Strategy 1:
Strategy 2:
NL: # of occupied bands
Computational load (on pen & paper)
Step 1:
Step 2:
Step 3:
Step 1:
Step 2:

## Slide 89: GW-BSE: what is it about?
DFT is a ground-state theory for electrons
But many processes involve exciting electrons:
Transport of electrons
Excited electrons: optical absorption promotes electron to higher energy
 The missing electron (hole) has + charge, attracts electron:
modifies excitation energy and absorption strength
e-
h+
“BSE” method solves this problem

## Slide 90: Would love to do GW on this interfacial oxide/semiconductor system…
Si interface with SrTiO3
Full unit cell

## Slide 91: Would love to do GW on this interfacial oxide/semiconductor system…
Si interface with SrTiO3
Full unit cell

## Slide 92
GW-Bare Exchange
Strategy 1:
Strategy 2:
NL: # of occupied bands
Biggest Computational load (on pen & paper)

## Slide 93
Performance
Total Wall Time (Seconds)
Step 2 – FFT P to G-Space
Step 1 – P in R-Space
Berkeley GW
OpenAtom
….Work in progress

## Slide 94
Performance
Total Wall Time (Seconds)
Step 2 – FFT P to G-Space
Step 1 – P in R-Space
….Work in progress
Number of Nodes
32 Threads per node on Vesta

## Slide 95: DFT: problems with excitations
Material | DFT-LDA | Expt. [1]
Diamond | 3.9 | 5.48
Si | 0.5 | 1.17
LiCl | 6.0 | 9.4
Energy gaps (eV)
[1] Landolt-Bornstien, vol. III; Baldini & Bosacchi, Phys. Stat. Solidi (1970).
[2] Aspnes & Studna, Phys. Rev. B (1983)
Solar spectrum

## Slide 96: Green’s functions successes
Material | DFT-LDA | GW* | Expt.
Diamond | 3.9 | 5.6 | 5.48
Si | 0.5 | 1.3 | 1.17
LiCl | 6.0 | 9.1 | 9.4
Energy gaps (eV)
* Hybertsen & Louie, Phys. Rev. B (1986)
Solar spectrum