## Slide 1: Charm++ as an Energy Efficient Runtime

## Slide 2: Interaction Between the Runtime System and the Resource Manager
Allows dynamic interaction between the system resource manager or scheduler and the job runtime system
Meets system-level constraints such as power caps and hardware configurations
Achieves the objectives of both datacenter users and system administrators

## Slide 3: Components of Charm++ with Its Interactions
Charm++ has three main components:
Local manager: tracks local information such as object loads, CPU temperatures
Load-balancing module: makes load-balancing
decisions and redistributes load
Power-resiliency module: ensures that the CPU temperatures remain below the temperature threshold, change the power cap

## Slide 4: Support for Proactive Cooling Decisions with Neural Network-Based Temperature Prediction
Bilge Acun1, Eun Kyung Lee1, Yoonho Park1, Laxmikant V. Kale2
1 IBM T.J. Watson Research Center
2 University of Illinois at Urbana-Champaign

## Slide 5: Motivation
Pressure of reducing the power consumption and carbon footprint of datacenters and supercomputers is increasing
Other expected problems include:
  Larger process variations, temperature variations
  More heat dissipation
  Denser nodes with different components in the node such as GPUs, co-processors that have different temperature, cooling characteristics

## Slide 6: Motivation
Temperature variations among cores:
  7 C in idle temperatures
  9 C in all active temperatures
  20 C idle/active mixed
Synchronous fan control:
  4 independent fans in the node
  Fans all act together and cause even further temperature variation
Reactive cooling behavior:
  54 W jump in fan power
  10 minutes stabilization time with a regular workload
7C
20 C
Notes: 3 different problems and opportunities for improvement

## Slide 7: Temperature Variation in Large Scale
Cori at NERSC – Intel Haswell
Minsky at IBM POWER8
Temperature distribution of 1800 cores

## Slide 8: Oscillatory Cooling Behavior
30 %
10 %
60 %
99 %
CPU Utilization
Workload starts

## Slide 9: Fan Behavior of Different Applications

## Slide 10: Why Temperature Modeling is Difficult?
There are lots of parameters affecting the core temperatures:
  Complex workloads
  Ambient temperature
  Core frequencies
  Fan speed level
  Physical layout
  Hardware variations
Combination of these parameters create an exponential modeling space
  10 different cores
  0-100 CPU utilization levels
  44 different frequency levels
  3000 RPM-10000 RPM fan speed levels
  4 fans
  (10^10) * 44 * (10^4) = ~ 2^52
Notes: core-to-core interactions

## Slide 11: Neural Networks for Temperature Modeling
Neural networks are good because:
  They can capture linear and non-linear behavior between input and output parameters
  They work well in noisy data
  They do not need for formulation of an objective function
Neural networks has been used in HPC for:
  Energy and power modeling [1]
  Performance modeling [2]
  Temperature modeling
    For GPU temperature modeling [3]
    For coarse-grained data center level modeling [4]
A. Tiwari, M. A. Laurenzano, L. Carrington, and A. Snavely. Modeling power and energy usage of HPC kernels. In Parallel and Distributed Processing Symposium Workshops & PhD Forum (IPDPSW), IEEE, 2012.
B. C. Lee, D. M. Brooks, B. R. de Supinski, M. Schulz, K. Singh, and S. A. McKee. Methods of inference and learning for performance modeling of parallel applications. In Proceedings of the 12th ACM SIGPLAN Symposium on Principles and Practice of Parallel Programming, PPoPP '07, 2007.
A. Sridhar, A. Vincenzi, M. Ruggiero, and D. Atienza. Neural network-based thermal simulation of integrated circuits on GPUs. IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems 31.
L. Wang, G. von Laszewski, F. Huang, J. Dayal, T. Frulani, and G. Fox. Task scheduling with ann-based temperature prediction in a data center: a simulation-based study. Engineering with Computers, 2011.

## Slide 12: Neural Networks for Temperature Prediction
Experimental Setup:
Firestone cluster at IBM with Power 8 processors
1 node = 2 sockets, 20 physical cores, 160 SMT cores
OCC, and BMC for temperature, power readings

## Slide 13: Neural Network Configuration and Validation
Other configurations include number of layers, and number of neurons.
We test different back-propagation algorithms with different time and memory requirements.

## Slide 14: Model Guided Proactive Cooling Decisions
Fan control
  This can reduce chip-to-chip temperature variations.
  What should be the fan speed level to be able keep the chips at a certain temperature limit?
Load balancing
  This can remove core-to-core, as well as chip-to-chip temperature variations.
  What would the core temperatures become if a certain amount of data is moved from one core to another?
DVFS
  Chip-level DVFS can reduce chip-to-chip, core level DVFS core-to-core temperature variations.
  What frequency level we need to set for the cores to stay under a temperature limit for a workload?

## Slide 15: Model Guided Proactive Cooling Decisions
Fan control
  This can reduce chip-to-chip temperature variations.
  What should be the fan speed level to be able keep the chips at a certain temperature limit?

## Slide 16: Proactive Fan Control Mechanism
Preemptive fan-control removes temperature peaks, and is able to keep the temperature as the same level as reactive fan control.
The key idea is cool the processor proactively, for example, before the application starts.
It can be done via job scheduler, and/or runtime without taking over the total control of the fan.
Notes: *independent fan control

## Slide 17: Power Reductions With Proactive Cooling
Power Reduction = Maximum Power – Stable Power
35% reduction in fan power

## Slide 18: Decoupling the Fans
BEFORE
AFTER
18% reduction in fan power

## Slide 19: Total Reduction in Fan Power
53% reduction in fan power on average

## Slide 20: Remaining Temperature Variation
DVFS?
Load Balancing?

## Slide 21: Temperature-Aware Load Balancing With Charm++
Load balancing can help reduce the temperature variations, but how do we decide how much load to move?
Charm++ [1] has an runtime database which stores:
  Number of tasks per process
  Load of each object (in terms of execution time)
  Communication load of each object
Load balancing is triggered periodically with customizable periods
We implement our temperature-aware model guided load balancing algorithm.
Load balancing has potential to remove both chip and core level variations.
1. B. Acun, et al. Parallel programming with migratable objects: charm++ in practice. In SC14: International Conference for High Performance Computing, Networking, Storage and Analysis, pages 647-658. IEEE, 2014.

## Slide 22: Conclusion
In summary, we propose:
  A neural-network based temperature prediction model
  Proactive cooling mechanisms:
    Fan control
    Load balancing
Our results shows:
  We can accurately predict core temperatures
  Peak fan power can be reduced by 53%
  Air cooling systems can be made more efficient

## Slide 23
Thank you!

## Slide 24: Comparison of Reactive vs Preemptive Fan Control
Preemptive fan-control removes temperature peaks, and is able to keep the temperature as the same level as reactive fan control.
The key idea is cool the processor proactively, for example, before the application starts.
It can be done via job scheduler, and/or runtime without taking over the total control of the fan.
Notes: *independent fan control

## Slide 25: Power Reductions in Preemptive Fan Control
Workload Starts
How early to set the cooling speed?
Peak fan power can be reduced by 54 Watts = 58% reduction in cooling power.
2790 Joules of energy is saved = Red area – black area
Notes: * add findings